## Slide 1: Automated Ream Opener
Mazin Chater
Youssef Jalwaj-Soubai
Abdullah Qureshi

## Slide 2: Overview 01 04 02 05 03 06
Previous limitations
The Issue
How requirements influenced the design
Requirements
Core functionality & how our design addresses the issue
Solution
A closer look at key components & code functionality
Features
How our solution will be used
Impact
Slideshow & Q/A
Wrap Up

## Slide 3: Problem
The Center for Disability Services Mailing Center processes an enormous amount of paper daily.
They use about 50,000-100,000 paper sheets per day.

## Slide 4: Problem
To get the paper, it must be manually opened from reams containing 500 sheets each.
This translates to about 100-200 reams per day.

## Slide 5: Problem
For disabled individuals, opening large volumes of reams presents many issues:
Damages internal paper
Paper cuts
Needs supervision

## Slide 6: System Requirements
The developed system must be safe to use
Safety
Fully functional, reliable, and adjustable
Functionality

## Slide 7: System Requirements
Simple and easy to use
Accessibility
Considered a bonus to balance efficiency with the worker’s sense of contribution
Timing

## Slide 8: Solution
How does it work?

## Slide 9: Function
3) Blades Slice Outside Layer
4) Unsealed Ream Returns
2) Green Button Initiates Operation
1) Insert Wrapped Ream Into Tray

## Slide 10: Safety Features
The carts are set in the back of the machine and only move towards the ream upon the start sequence
Analog blade holders ensure the blades are exposed to a minimum
If any issues arise, an emergency stop button ensures operations halt
Cart Position
Blade Position
Emergency Stop
The buttons are on the side of the machine to prevent any accidental presses
Button Position

## Slide 11: Key Improvements
 Disabled workers can independently use the device
 Design is reliable:
200+ reams have been opened with a ~95% success rate
 Takes only a press of a button & 30 seconds to open a ream

## Slide 12: Key Components
NEMA 23 Motor
Analog Blade Holders
Threaded Rod
Base for Tray
NEMA 17 Motors
Arduino, CNC Shield, DM542T

## Slide 13: Analog Blade Holders
 Allows blades to be just barely exposed
 Blades are easily interchangeable
 Blades can be adjusted to hit the outside layer of paper without damaging inner contents

## Slide 14: DM542T & CNC Shield
Drives top NEMA 23 stepper motor, threaded rod stepper motor, and the two side NEMA 17 motors.

## Slide 15: Circuitry

## Slide 16: Code

## Slide 17: Code

## Slide 18: Code

## Slide 19: Impact
The Center for Disability Services Mailing Center has expressed interest in hiring full-time disabled staff to use the machine
Current disabled employees have also been using it at the facility

## Slide 20: September

## Slide 21: October

## Slide 22: November

## Slide 23: December

## Slide 24: January

## Slide 25: February

## Slide 26: March

## Slide 27: April

## Slide 28: Thank you
Any questions?